OpenSIPS
clustering and balancing of media servers
Bogdan-Andrei Iancu
CEO Voice System
Founder OpenSIPS Project
bogdan.iancu@voice-system.ro

---
The story
Once upon a time there was a Switch and a PBX.......
........there was OpenSIPS and Yate.

---
The work
And they found out they complete each other ...
..... and decided to work out an easy integration.
They decide to make complex VoIP simpler to deploy.

---
Happy end
OpenSIPS developed a new functionality:
Load Balancing = call routing based on the realtime load of peer elements :
To control a cluster of heterogeneous PBX/media servers.
To be driven (via real-time feedback) by the cluster elements.

---
Load Balancing
What makes Load Balancing so special?
It is able to monitor in realtime the load (as ongoing calls) for each peer.
Instead of blind routing (like dispatcher module), it selects the target based on required resources and available load.

---
Load Balancing
What makes Load Balancing so special?
It is an interesting feature for a proxy as proxies are typically only transaction stateful (no dialog state).
It is able to provide failover to the peers from the cluster (even if the peers do not have any support) – detection and re-routing.
Can combine routing with LB functionality.

---
Clustering scenarios

---
Inbound- service LB
Fronting small/medium size PBX-based services for
scaling, LB and HA.
Incoming
calls
Yate /
Freeswitch /
Asterisk
boxes
OpenSIPS
Load Balancer

---
Inbound- Call Center
Controller for a Call Center
scaling, LB and HA.
Standard
operator
Incoming
calls
Business
operator
OpenSIPS
Load Balancer
Advanced
operator

---
Inbound- PSTN termination
Fronting pools/clusters of
scaling, LB and HA.
PSTN Gateway
Incoming
calls
OpenSIPS
Load Balancer

---
Outbound- Media Services
Fronting pools/clusters of heterogeneous media servers
scaling, LB and HA.
Announcement Servers
SIP
Proxy
Incoming
calls
Conference Servers
Media
calls
Voicemail Servers
OpenSIPS
Load Balancer

---
Outbound- GW routing
Routing to pools/clusters of heterogeneous Gateways
scaling, LB and HA.
PSTN GW
SIP
Proxy
Incoming
calls
H.323 GW
GW
calls
GSM GW
OpenSIPS
Load Balancer

---
Mixed scenario
Yate /
Freeswitch /
Asterisk
boxes
Incoming
calls
OpenSIPS
Load Balancer
PSTN GW
GSM GW
OpenSIPS
Load Balancer

---
Implementation details

---
Implementation Overview
Requires the dialog support (to count the ongoing calls for each peer) → dialog module.
Destinations/peer are identified by their SIP address.
The destinations are not homogeneous:
may have different capacities (supported calls)
may offer/provide different resources (services, functionalities)

---
Resources
Resources = capabilities of a destination/peer
Example:
a set of servers for media related services
each server may offer a combination of :
  - Transcoding
  - Voicemail
  - Conference
  - Announcement
  - PSTN GW
Mixed peer/destination : each of it may offer a different set of services/resources

---
Groups
LB Group = a set of peer/destinations used for a specific load-balancing scenario.
Example:
a mixed scenario with inbound and outbound LB
Group “0” may contain all the PBXs (inbound part)
Group “1” may contain all the GWs (outbound part)

---
Peer definition
Definition of each peer/destination contains:
the set of offered resources
for each resource, the capacity / maximum load
group it belongs to
the address (as SIP URI)
The capacity of a peer is defined as the number of concurrent calls the peer call handler (per resource).

---
Peer definition - example
Set of 4 peers:
30 channels for transcoding, 32 for PSTN GW
100 voicemail channels and 10 for transcoding
50 voicemail channels and 300 for conferencing
10 voicemail, 10 conference, 10 transcoding and 32 PSTN GW

---
Invoking LB
To invoke the Load Balancing logic, you need:
the LB group
the required resources
These are detected in the OpenSIPS routing script, based on whatever information is appropriated.
Example:
looking at RURI, if PSTN, VM or conference
looking at codecs from SDP, if transcoding is needed

---
 Load Balancing logic
Get the set of peers that belong to required group
Select from the set only the peers able to provide the required resources
For the selected peers, LB will evaluate the current load for each required resource
The winning peer is the one with the biggest value for the minimum available load per resource.

---
 LB logic – example I
Set of 4 peers:
30 channels for transcoding, 32 for PSTN GW
100 voicemail channels and 10 for transcoding
50 voicemail channels and 300 for conferencing
10 voicemail, 10 conference, 10 transcoding and 32 PSTN GW
when calling load_balance("1","transc;pstn") →
Step 1:
only boxes (1) and (4) will be selected at as they offer both transcoding and pstn (required resource)

---
 LB logic – example II
Step 2: Evaluating the load
(1) transcoding - 10 channels used; PSTN - 18 used
(4) transcoding - 9 channels used; PSTN - 16 used
evaluating available load (capacity-load) :
(1) transcoding - 20 channels free; PSTN - 14 free
(4) transcoding - 1 channels free; PSTN - 16 free
Step 3: Evaluating the minimum available load
(1) 14 - for PSTN
(4) 1 – for transcoding
Step 4: Select (1) as it has the biggest minimum available load

---
 LB logic – example III
14 free
16 free
20 free
1 free
18 used
16 used
10 used
9 used
30 trans
32 PSTN
10 trans
32 PSTN

---
 LB algorithms
Algorithms used for computing the available load:
Absolute value - the effective available load (maximum_load - current_load) is used in computing the load of each pear/resource.
Relative value - the relative available load (how many percentages are free) is used in computing the load of each pear/resource.

---
LB management

---
LB Failover
LB module can keep track of the failed peers:
if peer failed (timeout, 5xx reply), you can mark it as failed, so it will not be used anymore
after detecting a failed peer, you can resume the LB process (for the current call) over the remaining peers

---
LB Probing
LB module can probe/ping the peers:
probing can automatically re-enable failed peers when they they are back online
probing can detect failed peers in advance (and not at routing time) and disable them.

---
 Runtime changes
LB module provides external commands (MI) for:
reloading the whole LB data at runtime without affecting the LB process.
This allows addition/removal of peers, changes in resources.
to allow resizing the capacity of resource of a peer without requiring a reload of the whole data.
This “resizing” allows LB engine to receive feedback from the peer about their status.

---
 Runtime resize - Ex
Example 1:
a GW resource may increased or decreased by an admin following the addition or removal of cards from the GW box.
Example 2:
a monitoring tool running on a peer may trigger the resize (or even disable) of a resource following the detection of a failure on the peer box.

---
 Web management
OpenSIPS Control Panel – Load Balancing tool
inspect the status of the peers
enable/disable peers
apply runtime changes on the peers

---
Thank you for your attention
You can find out more at www.opensips.org
Questions are welcome
bogdan.iancu@voice-system.ro
bogdan@opensips.org